## Slide 1
Oil storage
Adam Jones
November 2016

## Slide 2: Introduction
2
Temporary storage
Types of temporary storage
Floating
Land
Specials
  Tanker rollover
  Equipment cleaning tanks (decontamination)
Storage ratios
Benefits
Questions & answers

## Slide 3: Temporary Storage
2

## Slide 4: Storage types
2
Floating
Land

## Slide 5: Floating storage
2
Floating
  Barge (FROST)

## Slide 6: Storage barge - FROST
2

## Slide 7: FROST – Sizes
Capacity
  5m3 (FR50)
  10m3
  25m3
  50m3
  100m3

## Slide 8: Materials
2
100% neoprene
Excellent resistance to hydrocarbons
Excellent resistance to salt water
High UV protection
Excellent flexibility
Excellent abrasion resistance
Vulcanised joints
Big operational range
  - 40oC to + 90oC

## Slide 9: Storage barge - FROST
Segmented inflatable sections enable the tank to remain afloat if one section is punctured

## Slide 10: Storage barge - FROST
2
Certified single point lifting sling provided
Only to be lifted while emptied
Horseshoe shape bow
Boat shape gives Excellent stability

## Slide 11: Storage barge - FROST
2
High visibility cover
Cover to prevent debris and water entering the tank
Skimmer discharge hose point in the top cover
Drainage point
Electric & diesel inflators available
Assisted deflation

## Slide 12: Storage barge - FROST
Easy to transport
Small storage volume
Multiple tanks can be used in a shuttle system to allow for continuous skimming operations

## Slide 13: Storage barge - FROST
Towing
  4 knots full
  10 knots empty
Multiple tanks can be towed in line

## Slide 14: Storage barge - FROST
Aluminium storage container
All equipment housed in the container
  Tank
  Top cover
  Inflator
  Repair kit
Removable sides for easy access
Lifting points & forkliftable

## Slide 15: Materials
2

## Slide 16: Storage ratios
2
Storage capacity vs skimmer recovery capacity
Customers skimmer recovery capability?
Storage capacity needs to be several times higher than skimming capacity in order to allow for continuous skimming operations.
20m3/hr skimmer could fill a 50m3 tank in 2 ½ hours
When the tank is full the skimming operation needs to stop while the tank is emptied or replaced (TIME!)

## Slide 17: Benefits
2
Large range of sizes available
Small & compact when stored
Wide range of applications
Can be used in a range of climatic conditions
Easy to manoeuvre
Quick and easy to inflate/set up

## Slide 18: Summary
2
Temporary storage
Types of temporary storage
Floating
Storage ratios
Benefits
Questions & answers

## Slide 19: Questions
Q & A

## Slide 20
Vikoma International Ltd
Kingston Works, Kingston Road East Cowes Isle of Wight PO32 6JS. UK
T: (0)1983 200560
E: sales@vikoma.com
W: www.vikoma.com